## Slide 1
Chart: Air concentration (ng/m3)
| < 0.1 | 0.1 - 1 | > 1 | Urban Chicago | Rural Michigan | Petroleum Refinery, Belgium | Rural Belgium | Urban Egypt | Coastal Oil Spill | Coastal Post-oil Spill
avg sum 14 PAHs$ | 316.836 | 226.1442 | 205.1567 | 121.6 | 20.6687 | 90.215 | 9.435 | 110.0384 | 6.3033 | 3.7135
Impact of fracking on PAH levels in ambient air
L. Blair Paulika, Carey E. Donalda, Brian W. Smitha, Lane G. Tidwella, Kevin A. Hobbiea, Laurel Kinclb, Erin N. Haynesc, Kim A. Andersona
aDepartment of Environmental and Molecular Toxicology, Oregon State University, Corvallis, Oregon, USA; bCollege of Public Health and Human Sciences, Oregon State University, Corvallis, Oregon, USA; cDepartment of Environmental Health, University of Cincinnati, Cincinnati, Ohio, USA
Introduction
Hypothesis
PAH levels increase as distance to an active fracking well decreases
Methods
Deployed low density polyethylene (LDPE) passive air samplers
  23 properties, for 3 weeks
  Trained landowners mailed to lab at OSU
  Cleaned LDPE with isopropanol, extracted with hexane
  Analyzed for 62 PAHs using GC-MS/MS
  Calculated air concentrations using performance reference compound data8
  Data grouped based on distance to closest active fracking well (Figure 2)
  “Active fracking well” = drilling, drilled, or producing
  Two sample t-tests performed on pairwise combinations of distance groups, α = 0.05
Fracking is increasing rapidly in the United States (Figure 1)
Studies suggest exposure to fracking-related volatile organic compounds are associated with health risks2,3
Polycyclic aromatic hydrocarbons (PAHs) may be of concern4-6
    Only one study measures ambient PAHs in relation to fracking7
Figure 1: Map of natural gas reserves in the United States1.
Fracking well pad
0.1 mile, “close” (n=5)
0.1-1.0 mile, “middle” (n=12)
1.0 mile, “far” (n=6)
C.E. Donald deploys passive samplers in air sampling cage (left); an air sampling cage with a producing fracking well pad in the background (right).
.
Figure 2: Visual explanation of three distance groups used in data analysis.
References
1Energy Institute of America, 2011; 2McKenzie LM, Witter RZ, Newman LS, & Adgate JL (2012) Human health risk assessment of air emissions from development of unconventional natural gas resources. Sci. Total Environ. 424:79-87. 3McKenzie LM, et al. (2014) Birth Outcomes and Maternal Residential Proximity to Natural Gas Development in Rural Colorado. Environmental health perspectives. 4Goldstein BD, et al. (2014) The Role of Toxicological Science in Meeting the Challenges and Opportunities of Hydraulic Fracturing. Toxicological Sciences:kfu061. 5Adgate JL, Goldstein BD, McKenzie LM (2014) Potential public health hazards, exposures and health effects from unconventional natural gas development. Environmental Science & Technology. 6Sommariva R, et al. (2014) Observations of the Release of Non-methane Hydrocarbons from Fractured Shale. Environmental Science & Technology. 7Colborn T, Schultz K, Herrick L, & Kwiatkowski C (2014) An Exploratory Study of Air Quality Near Natural Gas Operations. Hum. Ecol. Risk Assess. 20(1):86-105. 8Huckins JN, Petty JD, Booij K. (2006) Monitors of Organic Chemicals in the Environment (Springer, New York). 9Simcik MF, Zhang H, Eisenreich SJ, Franz TP (1997) Urban Contamination of the Chicago/Coastal Lake Michigan Atmosphere by PCBs and PAHs during AEOLOS. Environmental Science & Technology 31(7):2141-2147. 10Ravindra K, et al. (2006) Seasonal and site-specific variation in vapour and aerosol phase PAHs over Flanders (Belgium) and their relation with anthropogenic activities. Atmospheric Environment 40(4):771-785. 11Khairy MA & Lohmann R (2012) Field Validation of Polyethylene Passive Air Samplers for Parent and Alkylated PAHs in Alexandria, Egypt. Environmental Science & Technology 46(7):3990-3998. 12Tidwell LG, Allan SE, O'Connell SG, Hobbie KA, Smith BW, Anderson KA. (submitted 2014) PAH and OPAH Air-Water Exchange during the Deepwater Horizon Oil Spill. 13EPA, U. S. (2010). Development of a Relative Potency Factor (RPF) Approach for Polycyclic Aromatic Hydrocarbon (PAH) Mixtures. Washington, D.C. 14EPA, U. S. (2014). Memo: Recommended Default Exposure Factors. Office of Solid Waste and Emergency Response. Washington, D.C.
Acknowledgements
We acknowledge G. Wilson, R. Scott, J. Padilla, G. Points and M. McCartney of the OSU Food Safety and Environmental Stewardship Program for help with analysis, Dr. D. Rohlman of the OSU Environmental Health Sciences Center (EHSC) Community Outreach and Engagement Core (COEC), S. Elam from the University of Cincinnati (UC), EHSC COEC, J. Alden (UC) and Paul Feezel of Carroll Concerned Citizens, all for assistance with volunteer recruitment and communication, P. Kuhnell (UC) for mapping sample sites, and the volunteer participants in Ohio for making this study possible. This work was funded by the National Institute of Environmental Health Sciences grants to UC: P30-ES06096 and OSU: P30-ES000210.
Chart: Distance to active fracking well (miles)
| < 0.1 mile | > 0.1 and 1.0 mile | >1.0 mile
ΣPAHBaPeq (ng/m3) | 8.461 | 6.8213 | 5.3083
<0.1 0.1-1 >1.0
Average sum of 14 PAHs, compared to previous studies9-12. All data are vapor phase PAHs. PAHs closest to fracking activity are roughly an order of magnitude higher than in rural reference locations.
Average carcinogenic potency of PAHs. Benzo[a]pyrene equivalent concentrations (BaPeq), derived using the EPA’s Relative Potency Factors.13 Potency decreases significantly when samplers are farthest from fracking activity.
Implications
Sourcing ratios suggest PAHs near fracking wells are influenced by direct releases from the earth
  Elevated PAH levels may be related to fracking activity
All excess lifetime cancer risk estimates are >1/million, U.S. EPA’s conservative level of concern
  PAH levels are relevant to human health
Average sum of 62 PAHs. PAHs show a decreasing trend as distance to the closest active fracking well increases.
Distance to active fracking well (miles)
Chart: Air concentration (ng/m3)
| < 0.1 | 0.1 - 1 | > 1
sumPAH | 364.594 | 281.3417 | 250.31
Excess Lifetime Cancer Risk Estimates
3 Exposure Scenarios14
Residential maximum
262/million in close group 176/million in far group
Residential minimum
11/million in close group 7/million in far group
Outdoor worker
54/million in close group 36/million in far group
PAH sourcing ratios. Petrogenic mixtures are enriched in the more thermodynamically stable isomers, pyrene and phenanthrene. The predominant petrogenic signatures suggest PAH mixtures are predominantly influenced by direct releases of PAHs from the earth, not combustion.
Distance to active fracking well (miles)
A well is fracked in rural Ohio.
Results & Discussion